## Slide 1: Interconnection Networks: Topology
Prof. Natalie Enright Jerger

## Slide 2: Topology Overview
Definition: determines arrangement of channels and nodes in network
  Analogous to road map
Often first step in network design
Significant impact on network cost-performance
  Determines number of hops
    Latency
    Network energy consumption
  Implementation complexity
    Node degree
    Ease of layout

## Slide 3: Abstract Metrics

## Slide 4: Abstract Metrics
Use metrics to evaluate performance and cost of topology
Also influenced by routing/flow control
  At this stage
    Assume ideal routing (perfect load balancing)
    Assume ideal flow control (no idle cycles on any channel)

## Slide 5: Abstract Metrics: Degree
Switch Degree: number of links at a node
  Proxy for estimating cost
    Higher degree requires more links and port counts at each router
A
B
A
B
A
B
2
4
2,3,4

## Slide 6: Abstract Metrics: Hop Count
Path: ordered set of channels between source and destination
Hop Count: number of hops a message takes from source to destination
  Simple, useful proxy for network latency
    Every node, link incurs some propagation delay even when no contention
Minimal hop count: smallest hop count connecting two nodes

## Slide 7: Hop Count
Network diameter: large min hop count in network
Average minimum hop count: average across all src/dst pairs
  Implementation may incorporate non-minimal paths
    Increases average hop count

## Slide 8: Hop Count
Uniform random traffic
  Ring > Mesh > Torus
Derivations later
A
B
A
B
A
B
Max = 4
Avg = 2.2
Max = 2
1.33
Max = 4
1.77

## Slide 9: Latency
Time for packet to traverse network
  Start: head arrives at input port
  End: tail departs output port
Latency = Head latency + serialization latency
  Serialization latency: time for packet with Length L to cross channel with bandwidth b (L/b)
Approximate with hop count
  Other design choices (routing, flow control) impact latency
    Unknown at this stage

## Slide 10: Abstract Metrics: Maximum Channel Load
Estimate max bandwidth the network can support
  Max bits per second (bps) that can be injected by every node before it saturates
    Saturation: network cannot accept any more traffic
  Determine most congested link
    For given traffic pattern
    Will limit overall network bandwidth
    Estimate load on this channel

## Slide 11: Maximum Channel Load
Preliminary
  Don’t know specifics of link yet
  Define relative to injection load
Channel load of 2
  Channel is loaded with twice injection bandwidth
  If each node injects a flit every cycle
    2 flits will want to traverse bottleneck channel every cycle
    If bottleneck channel can only handle 1 flit per cycle
      Max network bandwidth is ½ link bandwidth
      A flit can be injected every other cycle

## Slide 12: Maximum Channel Load Example
Uniform random
  Every node has equal probability of sending to every node
Identify bottleneck channel
Half of traffic from every node will cross bottleneck channel
  8 x ½ = 4
Network saturates at ¼ injection bandwidth
A
C
D
B
E
G
H
F

## Slide 13: Bisection Bandwidth
Common off-chip metric
  Proxy for cost
  Amount of global wiring that will be necessary
  Less useful for on-chip
    Global on-chip wiring considered abundant
Cuts: partition all the nodes into two disjoint sets
  Bandwidth of a cut
Bisection
  A cut which divides all nodes into (nearly) half
  Channel bisection  min. channel count over all bisections
  Bisection bandwidth  min. bandwidth over all bisections
With uniform traffic
  ½ of traffic crosses bisection

## Slide 14: Throughput Example
Bisection = 4 (2 in each direction)
0
1
2
3
4
5
6
7
With uniform random traffic
  3 sends 1/8 of its traffic to 4,5,6
  3 sends 1/16 of its traffic to 7 (2 possible shortest paths)
  2 sends 1/8 of its traffic to 4,5
  Etc
Channel load = 1
Notes: Start here.

## Slide 15: Path Diversity
A
B
Multiple shortest paths between source/destination pair (R)
Fault tolerance
Better load balancing in network
Routing algorithm should be able to exploit path diversity
A
B
A
B
RA-B = 1
RA-B = 2
RA-B = 6

## Slide 16: Network Evaluation

## Slide 17: Evaluating Networks
Analytical and theoretical analysis
  E.g. mathematical derivations of max channel load
  Analytical models for power (DSENT)
Simulation-based analysis
  Network-only simulation with synthetic traffic patterns
  Full system simulation with real application benchmarks
Hardware implementation
  HDL implementation to measure power, area, frequency etc.
Measurement on real hardware
  Profiling and analyzing communication
Notes: Help them start thinking about projects…

## Slide 18: Evaluating Topologies
Important to consider traffic pattern
Talked about system architecture impact on traffic
If actual traffic pattern unknown
  Synthetic traffic patterns
    Evaluate common scenarios
    Stress test network
    Derive various properties of network

## Slide 19: Traffic Patterns
Historically derived from particular applications of interest
  Spatial distribution
  Matrix Transpose  Transpose traffic pattern
    di = si+b/2 mod b
    b-bit address, di: ith bit of destination
Notes: S = 0001
d = 0100
s = 0110
d = 1001

## Slide 20: Traffic Patterns Examples
Fast Fourier Transform (FFT) or sorting application  shuffle permutation
Fluid dynamics  neighbor patterns
Shuffle: di = si-1 mod b
Neighbor: dx = sx+ 1 mod k

## Slide 21: Traffic Patterns (3)
Uniform random
  Each source equally likely to communication with each destination
  Most commonly used traffic pattern
    Very benign
    Traffic is uniformly distributed
      Balances load even if topology/routing algorithm has very poor load balancing
      Need to be careful
  But can be good for debugging/verifying implementation
    Well-understood pattern

## Slide 22: Stress-testing Network
Uniform random can make bad topologies look good
Permutation traffic will stress-test the network
  Many types of permutation (ex: shuffle, transpose, neighbor)
  Each source sends all traffic to single destination
  Concentration of load on individual pairs
    Stresses load balancing

## Slide 23: Traffic Patterns
For topology/routing discussion
  Focus on spatial distribution
Traffic patterns also have temporal aspects
  Bursty behavior
  Important to capture temporal behavior as well
Motivate need for new traffic patterns

## Slide 24: Full System Simulation
NoC Simulator
Full System Simulator
NoC
Processor
Cache
Disk
Other Components
Application
Packets Sent
Packets Arrived
Feedback!
Accurate But Slow
Notes: Take aways

## Slide 25: Trace Simulation
NoC Simulator
Trace Simulator
Trace
NoC B
Packets Sent
NoC A
Processor
Cache
Disk
Other
Application
Faster But Less Accurate

## Slide 26: Traffic Patterns
NoC Simulator
NoC
Synthetic Traffic Driver
Application
Traffic Pattern
Uniform Random
Bit Complement
Bit Reverse
Bit Rotation
Shuffle
Transpose
Tornado
Neighbour
Very Fast But Inaccurate

## Slide 27: Common Topologies

## Slide 28: Types of Topologies
Focus on switched topologies
  Alternatives: bus and crossbar
  Bus
    Connects a set of components to a single shared channel
    Effective broadcast medium
  Crossbar
    Directly connects n inputs to m outputs without intermediate stages
    Fully connected, single hop network
    Component of routers

## Slide 29: Types of Topologies
Direct
  Each router is associated with a terminal node
  All routers are sources and destinations of traffic
Indirect
  Routers are distinct from terminal nodes
  Terminal nodes can source/sink traffic
  Intermediate nodes switch traffic between terminal nodes
To date: Most on-chip networks use direct topologies

## Slide 30: Torus (1)
K-ary n-cube: kn network nodes
N-Dimensional grid with k nodes in each dimension
3-ary 2-cube
3-ary 2-mesh
2,3,4-ary 3-mesh

## Slide 31: Torus (2)
Map well to planar substrate for on-chip
Topologies in Torus Family
  Ex: Ring -- k-ary 1-cube
Edge Symmetric
  Good for load balancing
  Removing wrap-around links for mesh loses edge symmetry
    More traffic concentrated on center channels
Good path diversity
Exploit locality for near-neighbor traffic

## Slide 32: Hop Count
Average shortest distance over all pairs of nodes
Torus:
  For uniform random traffic
    Packet travels k/4 hops in each of n dimensions
Mesh:

## Slide 33: Torus (4)
Degree = 2n, 2 channels per dimension
  All nodes have same degree
Total channels = 2nN

## Slide 34: Channel Load for Torus
Even number of k-ary (n-1)-cubes in outer dimension
Dividing these k-ary (n-1)-cubes gives a 2 sets of kn-1 bidirectional channels or 4kn-1
½ Traffic from each node cross bisection
Mesh has ½ the bisection bandwidth of torus
Notes: 4k^(n-1) = 4*k^n*k^-1 = 4N/k
N/2 traffic is going to be distributed over 4N/k channels so the load is (N/2)/(4N/k) = N/2 * k/4N
Mention adversarial traffic pattern for torus… some kind of permutation…

## Slide 35: Deriving Channel Load: 4-ary 2-cube
Divide network in half
Number of bisection channels
  8 links, bidirectional = 16 channels
½ traffic crosses bisection
N/2 traffic distributed over 16 links
Channel load = ½
  Loaded at twice injection bandwidth
Notes: Channel load of 2
  Channel is loaded with twice injection bandwidth
  If each node injects a flit every cycle
    2 flits will want to traverse bottleneck channel every cycle
    If bottleneck channel can only handle 1 flit per cycle
      Max network bandwidth is ½ link bandwidth
      A flit can be injected every other cycle

## Slide 36: Torus Path Diversity
2 edge and node disjoint minimum paths
2 dimensions*
*assume single direction for x and y
NW, NE, SW, SE combos
Notes: Assumes one-way routes (choose starting direction for X and Y, 6 routes with X east and Y south). 6 more routes for X west and Y south),

## Slide 37: Mesh
A torus with end-around connection removed
Same node degree
Bisection channels halved
  Max channel load = k/4
Higher demand for central channels
  Load imbalance

## Slide 38: Butterfly
Indirect network
K-ary n-fly: kn network nodes
Routing from 000 to 010
  Dest address used to directly route packet
  Bit n used to select output port at stage n
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
0
1
0
2-ary 3-fly
2 input switch, 3 stages
Notes: all channels are unidirectional and flow from left to right

## Slide 39: Butterfly (2)
No path diversity
  Can add extra stages for diversity
    Increase network diameter
0
x0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
x1
x2
x3
10
11
12
13
20
21
22
23
00
01
02
03

## Slide 40: Butterfly (3)
Hop Count
  LogkN + 1
  Does not exploit locality
    Hop count same regardless of location
Switch Degree = 2k
Requires long wires to implement

## Slide 41: Butterfly: Channel Load
Hmin x N: Channel demand
  Number of channel traversals required to deliver one round of packets
Channel Load  uniform traffic
  Equally loads channels
  Increases for adversarial traffic
Notes: Hmin = n+1

## Slide 42: Butterfly: Deriving Channel Load
Divide network in half
Number of bisection channels: 4
4 nodes (top half) send ½ traffic to lower half
Distributed across 2 channels (C)
Channel load = 1
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23

## Slide 43: Butterfly: Channel Load
Adversarial traffic
  All traffic from top half sent to bottom half
  E.g. 0 sends to 4, 1 sends to 5
Channel load: 2
  Loaded at ½ injection bandwidth
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23

## Slide 44: Clos Network
3-stage indirect network
  Larger number of stages: built recursively by replacing middle stage with 3-stage Clos
Characterized by triple (m, n, r)
  M: # of middle stage switches
  N: # of input/output ports on input/output switches
  R: # of input/output switches
Hop Count = 4

## Slide 45: Clos Network
nxm input switch
nxm input switch
nxm input switch
nxm input switch
rxr input switch
rxr input switch
rxr input switch
rxr input switch
rxr input switch
mxn output switch
mxn output switch
mxn output switch
mxn output switch

## Slide 46: Clos Network
Strictly non-blocking when m > 2n-1
  Any input can connect to any unique output port
r x n nodes
Degree
  First and last stages: n + m, middle stage: 2r
Path diversity: m
Can be folded along middle switches
  Input and output switches are shared

## Slide 47: Folded Clos (Fat Tree)
Bandwidth remains constant at each level
Regular Tree: Bandwidth decreases closer to root

## Slide 48: Fat Tree (2)
Provides path diversity

## Slide 49: Application of Topologies to On-Chip Networks
FBFly
  Convert butterfly to direct network
Swizzle switch
  Circuit-optimized crossbar
Rings
  Simple, low hardware cost
Mesh networks
  Several products/prototypes
MECS and bus-based networks
  Broadcast and multicast capabilities

## Slide 50: Implementation
Folding
  Equalize path lengths
    Reduces max link length
    Increases length of other links
0
1
2
3
0
1
2
3

## Slide 51: Concentration
Don’t need 1:1 ratio of routers to cores
  Ex: 4 cores concentrated to 1 router
Can save area and power
Increases network complexity
  Concentrator must implement policy for sharing injection bandwidth
  During bursty communication
    Can bottleneck

## Slide 52: Implication of Abstract Metrics on Implementation
Degree: useful proxy for router complexity
  Increasing ports requires additional buffer queues, requestors to allocators, ports to crossbar
  All contribute to critical path delay, area and power
  Link complexity does not correlate with degree
    Link complexity depends on link width
    Fixed number of wires, link complexity for 2-port vs 3-port is same

## Slide 53: Implications (2)
Hop Count: useful proxy for overall latency and power
  Does not always correlate with latency
    Depends heavily on router pipeline and link propagation
  Example:
    Network A with 2 hops, 5 stage pipeline, 4 cycle link traversal vs.
    Network B with 3 hops, 1 stage pipeline, 1 cycle link traversal

## Slide 54: Implications (2)
Hop Count: useful proxy for overall latency and power
  Does not always correlate with latency
    Depends heavily on router pipeline and link propagation
  Example:
    Network A with 2 hops, 5 stage pipeline, 4 cycle link traversal vs.
    Network B with 3 hops, 1 stage pipeline, 1 cycle link traversal
Hop Count says A is better than B
But A has 18 cycle latency vs 6 cycle latency for B

## Slide 55: Implications (3)
Topologies typically trade-off hop count and node degree
Max channel load useful proxy for network saturation and max power
  Higher max channel load  greater network congestion
  Traffic pattern impacts max channel load
    Representative traffic patterns important
  Max power: dynamic power is highest with peak switching activity and utilization in network

## Slide 56: Topology Summary
First network design decision
Critical impact on network latency and throughput
  Hop count provides first order approximation of message latency
  Bottleneck channels determine saturation throughput